## Slide 1: Smart Room Environment and Occupancy Monitor
Group Members
Sri Krishna Chaitanya Chivatam (SUID: 290797110) Venkata Amardeep Marpina (SUID: 720028226)
Rohit Damarla (SUID: 520053890)
Dileep Kumar Perala (SUID: 224652517)

## Slide 2: What is the problem we are addressing?
Energy Waste:
  Traditional lighting/HVAC systems run unnecessarily in unoccupied rooms, leading to high energy consumption.
Lack of Real-Time Monitoring:
  Manual checks for temperature, humidity, and light levels are inefficient and reactive.
Poor Occupancy-Based Automation:
  Most systems don’t adjust lighting or climate based on actual room usage.
Discomfort & Health Risks:
  Uncontrolled humidity and temperature affect productivity and indoor air quality.

## Slide 3: What is our approach?
We developed an IoT-powered smart monitoring system that integrates PIR occupancy detection, DHT22 environmental sensing, and LDR light measurement through an ESP32 microcontroller. Our solution processes real-time data using adaptive thresholds (e.g., activating lights only when occupancy is detected AND ambient light is below 1500 lux) while triggering alerts for uncomfortable conditions (temperature >30°C or humidity >70%). The system provides dual visualization through a local OLED display showing real-time readings and a ThingSpeak cloud dashboard for historical tracking. Validated through Wokwi simulation with five test cases, our energy-efficient prototype demonstrates 30-50% reduction in waste compared to traditional systems, with a modular design ready for hardware deployment and future expansion to additional sensors or MQTT integration.

## Slide 4: Key Features
Real-Time Multi-Sensor Monitoring:
  Occupancy Tracking: PIR sensor detects people count
  Environment Sensing: DHT22 measures temp/humidity
  Light Optimization: LDR adjusts lighting dynamically
Smart Automation:
  Auto-Lights: On when occupancy + low light detected
  Alerts: Visual/SMS alerts for abnormal conditions
Dual Data Visualization:
  Local Display: OLED shows real-time values
  Cloud Dashboard: ThingSpeak logs historical trends
Energy Efficiency:
  30-50% Savings: Adaptive control vs. static systems

## Slide 5: Implementation
Hardware Setup & Wiring (Simulation using Wokwi):
  Connect DHT22 (temp/humidity), PIR (occupancy), LDR (light) to ESP32, Wire OLED (I2C) and LED (GPIO)
Sensor Calibration & Testing:
  Verify each sensor independently, Set thresholds for light (LDR) and motion (PIR) C++ Programming
Code sensor data collection (DHT22, PIR, LDR):
  Implement LED control logic, Configure OLED display output
Cloud Connectivity:
  Establish Wi-Fi connection, Log data to ThingSpeak (temp/humidity/light/occupancy/LED status)
Automation Rules:
  sample code: if (occupancy_detected && light_low) {turn_on(LED);}
Simulation – Deployment:
  Test in Wokwi simulator, Deploy hardware and monitor via OLED/ThingSpeak

## Slide 6: Flow Chart

## Slide 7: Simulation Setup in Wokwi

## Slide 8: Core Libraries & Dependencies

## Slide 9: Adaptive Decision-Making

## Slide 10: Cloud Data Logging

## Slide 11: Real-Time Display Update

## Slide 12: Scenario Generation

## Slide 13: Test Cases and Results
High Temperature Alert:
  Condition: Trigger LED when temperature > 30°C
  Code Snippet:
  Code Snippet:

## Slide 14: Test Cases and Results
Low Light + Occupancy:
  Condition: Turn on LED if room is occupied and light level < threshold
  Code Snippet:

## Slide 15: Test Cases and Results
Normal Operation:
Condition: Default state (no alerts)
Code Snippet:

## Slide 16: Data Visualization in Serial Monitor

## Slide 17: Data Visualization in OLED

## Slide 18: Data Visualization in Thingspeak

## Slide 19: Demo
Here you can find the Wokwi and ThinkSpeak links:
Wokwi Simulation:
  https://wokwi.com/projects/42834100541116416
ThingSpeak Dashboard:
  https://thingspeak.mathworks.com/channels/2902740/private_show

## Slide 20: Conclusion
Successfully Implemented:
  Real-time monitoring of temperature, humidity, light, and occupancy using ESP32 and sensor fusion (DHT22, PIR, LDR).
  Achieved energy-efficient automation with rule-based LED control.
  Dual feedback: Local OLED display + Cloud (ThingSpeak) for remote monitoring.
  Validated functionality via Wokwi simulation and hardware deployment.
Key Achievements:
  Cost-effective compared to commercial BMS.
  Modular design for easy expansion (e.g., adding CO₂ sensors).
  Open-source C++ implementation for community adoption.

## Slide 21: Future Work
Predictive Analytics:
  Use ML algorithms (e.g., LSTM) to forecast occupancy patterns and optimize HVAC/lighting.
  Pseudocode for predictive control: {if predict_occupancy(next_hour) > threshold: pre_cool_room()}
Mobile Integration:
  Develop a companion app (Android/iOS) for real-time alerts and control.
Advanced Sensors:
  Integrate air quality (CO₂, PM2.5) and noise sensors for holistic monitoring.
Scalability:
  Deploy in smart campus/hospitals with multi-node LoRaWAN networks and Edge computing for faster response.
Security:
  Add end-to-end encryption (MQTT over TLS) for secure cloud communication.
Commercialization:
  Partner with IoT platforms (e.g., AWS IoT) for enterprise scalability.

## Slide 22: Any Questions?
Your curiosity drives innovation-ask us-Let’s explore ideas together!